MAJOR PROJECT – EC498

IMPLEMENTATION OF LOW DENSITY PARITY CHECK CODES

Team Members

Akash A (191EC102)
Navratan (191EC133)

Mentor

Professor John D’Souza

National Institute of Technology, Karnataka Surathkal
NH66, Srinivasnagar Surathkal
Mangalore Karnataka – 575025

SECTION I: PROJECT OBJECTIVES

This work aims to study a particular class of capacity – achieving codes called Low Density Parity Check (LDPC) codes. The authors have attempted to study and implement LDPC codes at the software and circuit level. Extensive study has been done on the methods of construction of LDPC codes that can give good performance and at the same time can be implemented with reasonable complexity. Software implementation of the encoder and decoder is performed and the resulting code is tested by modelling an Additive White Gaussian Noise (AWGN) channel. Results are presented in terms of Eb v/s No curves to show the correct operation of the circuit. The code written is efficient in the fact that it can be extended to larger block lengths with minimal modifications. To show the extensibility of the code, four different LDPC codes are simulated by simply changing the parameters of the code. Finally, to demonstrate the correctness of results, comparison with previous works using similar procedures and block lengths is performed.

SECTION 2: LITERATURE SURVEY

The first mention of LDPC codes appears in a landmark paper by Robert G. Gallager in 1963. Gallager showed that such LDPC codes when extended to large block lengths could approach Shannon’s capacity limit for noisy channel transmission while having reasonable implementation complexity. However, resources at the time were not sufficent for the practical realization of these codes. Thus, LDPC codes did not receive much attention from the information theory community until the late 1990s where improvements in semiconductor technology made it possible to practically realize circuits for encoding and decoding. Ever since, extensive research has been done in this field to construct LDPC codes that have some algebraic structure and can be easily implemented in hardware. This section summarizes the study performed by the authors for implementation of these LDPC codes and explains the reasons for the selection of specific methods.

Implementation of any LDPC code involves three steps – first, a sparse parity check matrix must be constructed which is guaranteed to perform well. Then algorithms for encoding must be realized by finding a suitable generator matrix for the code. The last step is to perform the decoding and error correction. Research regarding the construction of the parity check matrix mainly focusses on two factors – the requirement of not having short cycle lengths (large girth) in the code which results in better decoder performance and the second requirement of having a large minimum distance which gives a better error correcting capability for the code. Methods for construction of LDPC codes are classified into two subclasses in literature – Graph based algorithms and Algebra Based Algorithms. The main motive behind either of these is to achieve codes with wide girth. Graph based algorithms have the flexibility that they can be used to achieve parity check matrices of any desired size. On the other hand algebra based algorithms can realize codes of only specific sizes corresponding to the propperties of the algebraic structure. However, due to the structure associated with algebra based algorithms, they are easier to implement.

2.1: Construction of the Parity Check Matrix

Xiao-Yu Hu and his fellow researchers contributed an algorithm called the Progressive Edge Growth (PEG) algorithm based on greedy approach which can be used to construct LDPC codes without any short length cycles. This is the main graph – based algorithm available in literature and several modifications have been attempted to improve this algorithm in subsequent years. M.P.C. Fossorier and his fellow researchers in a correspondence published in 2004 proposed a subclass of LDPC codes called Quasi Cyclic LDPC (QCLDPC) codes based on circulant permutation matrices which have relatively low implementation complexity. Further, the research work provided necessary and sufficient conditions to realize codes with girth at least 4, 6, 8, 10 and 12. He also showed mathematically that QC LDPC codes cannot have a girth larger than 12. Research in subsequent years has found a plethora of algorithms that can construct a sparse matrix of circulants based on modern algebra.

Zongwang Li and B.V.K. Vijaya Kumar proposed a method in 2004 for adapting the Progressive Edge Growth (PEG) algorithm to the quasi – cyclic case. This method could combine the advantage of better performance of graph – based approach with low implementation complexities of structured LDPC codes. This method was implemented by authors but the resulting code did not guarantee a large girth in every case and could lead to poor performance of the code when decoded iteratively. Thus, the authors decided to completely shift to algebraic techniques to have simpler implementation complexities. In 2006, Zongwang Li, Li Cheng, et al proposed a method based on finite geometries for the construction of QCLDPC codes that would have a girth of at least 6. This method was based on the intersections of lines in a 3D Euclidean geometry and has been adopted as a standard LDPC code by NASA for deep space communication. However, the geometry associated with the construction of this code requires a high level of mathematical understanding and hence was not adopted by the authors. In 2007, Lan Lan, Lingqui Zeng, et al proposed a simple algorithm based on the primitive elements of finite fields to constructed QCLDPC codes of girth at least 6. This method has been adopted by the authors and is described in detail in the later sections of this report. The method has gained wide popularity owing to the simplicity of its construction and great performance. In following years, several other methods of algebraic construction have also been proposed with notable ones studied by the authors being a method based on Sidon sequences proposed by GuoHua Zhang, Rong Sun, et al in 2012 and another based on the Chinese remainder theorem proposed in 2014 by Yuan Hua Liu, Mei Ling Zhang, et al.

In the recent years, focus has been shifted towards construction of multi – rate LDPC codes which are already in systematic form. Such codes have been adopted in the 5G standard. The construction of the exponent matrices of multi – rate LDPC codes is described by Huaan Li, Baoming Bai, et al in a paper published in 2018. Since the code is already in systematic form, the encoding process becomes very simple as it can be done directly using the parity check matrix. Further, the parity check matrix has provisions for shortening, puncturing and extension which makes it possible to adapt a single parity check matrix to multiple code rates which is the case of the LDPC codes used in 5G new radio. The construction of the base matrices of such a code is based on more advanced techniques such as Density Evolution (DE) which are guaranteed to produce a base matrix that will perform well and has a structure (systematic and double – diagonal) that permits easy encoder implementation. Due to the involved mathematics associated with the construction of such codes, these methods were avoided by the authors. Further, the recent research suggests a migration towards Spatially Coupled LDPC (SCLDPC) codes where systematic encoding is not possible. With a view towards making implementation of SC LDPC easier, the authors focussed on implementing just Quasi Cyclic LDPC codes without using the systematic form.

In recent years, the focus has shifted towards the implementation of Spatially Coupled LDPC codes. An explanation of such LDPC codes can be found in a 2015 correspondence by David G. M. Mitchell, Michael Lentmaier, Daniel J. Costello, et al. The construction of SC LDPC codes that are easy to implement is still an open question and extensive research is currently being performed to find such methods. The authors have a keen interest to find out such sparse matrices and this forms a part of their future work related to this project.

2.2: Encoding and Decoding Strategies

In 2006, Zongwang Li, Lei Chen, Lingqi Zeng et al proposed a method to find the generator matrix for a QC LDPC code in systematic circulant form. Further, they described a hardware realization for the encoder using a simple shift register based circuit. The authors have adopted this method for implementation since the parity check matrices constructed were mainly in non – systematic form. If the parity check matrix is in systematic form, the encoding can be done simply from the parity check matrix form using XOR gates. There is another structure usually adopted in literature that gives good performance known as the double diagonal or raptor like structure. This method also provides for simple encoding by solving some simple binary equations to get the parity check bits. In the 5G standard, a combination of systematic and double diagonal structure is adopted in the parity check matrix. The method for encoding is described by Huaan Li, Baoming Bai, et al in a paper published in 2018.

For decoding, there are several approaches used. The main implementation is a soft decoder which propagates log likelihood ratios over the Tanner graph. Gallager in his original paper derived the formula for these log likelihood ratios. However, these equations are very complex to implement in hardware and a lot of approximations have been made over recent years to make the implementation simpler. One such approximation is the sum product algorithm proposed by F. Kschischang, B. Frey, and H.-A. Loeliger in 2001. Another algorithm is the min sum algorithm that was adopted by the authors which is a very simple algorithm with low implementation complexity in hardware. The decoding can either be carried out on the entire parity check matrix or layer by layer which is known as the layered decoding approach. The authors have adopted the layered decoding approach since it has been shown to converge faster under iterative decoding. This algorithm was proposed by D.E. Hocevar et al in 2004. There are also some modified algorithms proposed for decoding of SCLDPC codes with reduced time and space complexities which lead to capacity – approaching performance. One such algorithm is the windowed decoding approach proposed by A. R. Iyengar, P. H. Siegel, R. L. Urbanke and J. K. Wolf in 2011.

The authors have adopted the method of non – systematic encoding followed by layered decoding using the belief propagation algorithm due to its ease of hardware implementation as well as the possibility of extension of the methods used to spatially coupled LDPC codes.

SECTION 3: INTRODUCTION

During the process of telecommunication, there are often errors introduced in the transmitted data no matter how good the channel may be. This occurs due to various sources of noise which may be either additive or multiplicative. At the receiver, our task is to inspect the received data and determine if any errors have occured and if yes, we further need to correct these errors so that we can obtain the transmitted data with as much integrity as possible. Errors may also occur with time when data is stored in memory. The process of error detection and correction is possible in the case of digital communication where we trasmit either 1’s or 0’s and hence the received data is also either a 0 or a 1. In analog communication schemes, error detection and correction is not possible since the transmitted data is in the form of continuous voltages or currents. This is one of the reasons why digital communication is widely used today. The process of error detection and correction is carried out by introducing extra bits known as parity bits into the channel along with the information bits. The parity bits add redundancy to the data in a structured way that facilitates reliable reconstruction of data at the receiver. The methodology of adding this redundancy is studied in the field of Error Control Codes and there are several classes of these codes available today which can achieve exceedingly low probabilities of error.

The question then arises as to what is the maximum capability can error correcting code can achieve. This answer was provided by Claude Shannon in his paper in 1948 where he showed that for a given channel with a particular bandwidth and signal to noise ratio (SNR), we could have reliable data transmission with arbitrarily small probabilities of error if the rate at which we are transmitted data is kept smaller than a maximum value. This maximum value is called the capacity of the channel and is related to the bandwidth and the SNR. For AWGN channels, the relation is given by:

C ~ = ~ B ~ log_2 (1 ~ + ~ SNR)

Shannon showed that by using an arbitrarily long information block and by assigning an even longer code word to this block at random so that the final rate at which we are transmitting the information R is less than C, we can achieve almost zero probabilities of error. The limiting capacity value is called the Shannon limit and the process of forming blocks of information bits and then encoding them leads to a class of error control codes called block codes. Although this method helps us achieve our purpose, the complexity of encoding and decoding is huge for longer codes due to the large number of gates to be used. If the number of information bits is k, we would need to store a look up table with 2k code words which would use too much storage for k values in the order of 1000. In order to reduce the complexity, we generally go for a subclass of block codes called linear block codes where we pick a set of k codewords that form a subspace and use the span of this subspace to generate all the 2k code words. This is case for binary codes and the process can be easily extended to larger codes as well. The k code words are stored in memory in the form of a generator matrix G and logic is implemented at the encoder to generate linear combinations of the generator matrix to form the code words. In general, a code vector v can be obtained from the informatio vector u by premultiplying the generator matrix with the information vector.

bold{v} ~ = ~ bold{u}.bold{G}

Thus, the encoding complexity is simplified. The generator matrix is usually in systematic form where the information bits are grouped together to form a block followed by a block of parity bits. The systematic generator matrix is of the form:

G = [Ik | P]

Here, Ik is a k x k identity matrix and P is a k x (n-k) parity check submatrix.

Similar to a generator matrix for encoding, every linear block code also has another matrix specified for it called the parity check matrix H. This matrix is formed by the null space of the code vectors in the generator matrix. Since the entire linear block code is formed by the row space of the generator matrix, any code vector in the linear block code must lie in the null space of the parity check matrix. Thus, at the decoder, to check if the code vector received is a valid code vector we can simply check if it lies in the null space of the parity check matrix. This comutation is called the syndrome s and is used for error detection. If there is an error, we will then need to identify the error and correct it. The parity check matrix in systematic form and the formula for syndrome computation is as shown below:

H = [PT | In-k]

s = r.HT

An optimal algorithm for decoding any linear block code is called maximum likelihood decoding where we compare the received code vector with each of the valid code vectors and select the valid code vector that has minimum distance from it. However, if we choose the information vector size to be large to get capacity achieving codes, there are a huge number of valid code vectors and hence the comparison becomes very difficult to perform. The solution to this issue was proposed by Gallager in the 1960s where he proposed the use of sparse parity check matrices and suggested an iterative decoding algortithm named Belief Propagation (BP) that was suboptimal, but could be implemented with low complexity. He showed that with a large number of iterations, the iterative algorithm could perform as well as the maximum likelihood decoding scheme. Such codes are called Low Density Parity Check (LDPC) codes and are the topic of discussion of this report.

3.1: Low Density Parity Check Codes

LDPC Codes are a subclass of error control codes for which the parity check matrix is a sparse binary matrix. The number of non-zero entries in the parity check matrix must be smaller than the number of rows in the matrix for the matrix to be considered sparse. Although the parity check matrix is sparse, it is not generally in systematic form. Thus, there is no guarantee that the parity check matrix in its systematic form or the systematic generator matrix is sparse. This means that a large number of code word bits are not zero after decoding and thus, the code will still have structured redundancy which helps to identify and correct errors.

The parity check matrix in its sparse form is generally represented in the form of a bipartite graph called the Tanner graph which offers a lot of intuition while performing the encoding and decoding processes as well as the theoretical analysis of LDPC codes using techniques such as Density Evolution (DE). In the Tanner graph, the rows of the parity check matrix are represented on the right hand side in the form of check nodes. The columns of the parity check matrix are represented by convention on the left hand side in the form of bit nodes. For every non-zero entry in the parity check matrix, a connection is made between the bit node and check node corresponding to the row and column at which the entry occurs. The Tanner Graph corresponding to a simple (6, 3) libear block code is as illustrated below along with its parity check matrix:

        H = left ( matrix{1 # 0 # 0 # 0 # 1 # 1 ##0 # 1 # 0 # 1 # 0 # 1 ##0 # 0 # 1 # 1 # 1 # 0} right )

An important observation that we can make from the Tanner graph is called the girth of the code. Girth is defined as the length of the shortest cycle in the Tanner graph that has the same start and end node and no other nodes or edges are repeated in the path. It is intuitive to see that due to the bipartite nature of the Tanner graph, the girth will always be an even number. Further, since there can only be a single direct edge between two nodes, girth of two is not possible. Thus, the Tanner graph has a girth of at least four. The girth of the parity check matrix is an important property which affects the performance of the code. The decoding of LDPC codes is generally based on belief propagation where probabilities are passed along the edges of the Tanner graph back and forth between the bit and check nodes. The prescence of cycles in the graph affects the independence of the passed probabilities and leads to poor performance. Thus, there is a need to realize parity check matrices with wide girth. In the parity check matrix we had described in the example above, we can observe that there is no cycle of length four. The girth of the Tanner graph is 6. One cycle of length 6 in the Tanner graph is illustrated below:

Example of Cycle in the Tanner Graph

It is common to define some structure in the parity check matrix of an LDPC code. One such way is where the number of ones in each row and column are equal. Such an LDPC code is called a regular LDPC code and is generally denoted as a (J, K) regular LDPC code where the parity check matrix contains J ones in each column and K ones in each row. If the parity check matrix does not contain a uniform number of ones in each row and column, the LDPC code realized is said to be an irregular LDPC code. It has been observed that regular LDPC codes are generally not capacity – achieving codes but give good performance in the threshold region of the BER – SNR curve while irregular LDPC codes are capacity–achieving and give good performance in the waterfall region but they tend to have large thresholds. Recent research attempts to exploit the advantages of both regular and irregular LDPC codes using Spatially Coupled LDPC (SCLDPC) codes where memory is introduced into the encoder by introducing cross linking connections between indivual Tanner graphs of the linear block code. SCLDPC codes have been shown to outperform both regular and irregular LDPC codes in both the waterfall and threshold regions and are capacity – achieving. An example of a (2, 4) regular parity check matrix is as shown below:

H = left(matrix{1 # 0 # 0 # 1 # 1 # 0 # 1 # 0 ##0 #1 # 1 # 0 # 0 # 1 # 0 # 1 ##0 # 1 # 0 # 1 # 1 # 0 # 0 # 1 ##1 # 0 # 1 # 0 # 0 # 1 # 1 # 0}right)